## Slide 1: Evaluating Asymmetric Multiprocessing for Mobile Applications
Songchun Fan, Benjamin Lee
Duke University

## Slide 2: Mobile Processor Trends

## Slide 3: Case for Multicore
1. Single Core
2. Double Cores
  2x cores
  2x power
  2x throughput
3. Tune Design
  Reduce voltage, frequency
  Simplify microarchitecture
  -1% perf, -3% power

## Slide 4: Multicore Challenges
Limited Parallelism
  68% time with one core
  Gao et al. ISPASS’15
Chart: 
| 1 core | 2 cores | 3+ cores
Use (%) | 68.7 | 24.3 | 6.9

## Slide 5: Multicore Challenges
Limited Parallelism
  68% time with one core
  Gao et al. ISPASS’15
Heterogeneous Apps
  Compute- vs non-compute intensive
Chart: 
Non-Compute Intensive
Compute Intensive

## Slide 6: Multicore Challenges
Limited Parallelism
  68% time with one core
  Gao et al. ISPASS’15
Heterogeneous Apps
  Compute- vs non-compute intensive
Heterogeneous Events
  User inputs trigger computation

## Slide 7: Heterogeneity for Efficiency
Define big and little core
Different voltage, frequency
  Qualcomm S800 Series
800MHz
1GHz

## Slide 8: Heterogeneity for Efficiency
Define big and little core
Different voltage, frequency
  Qualcomm S800 Series
Different microarchitecture
  NVIDIA Tegra 3
  Samsung Exynos 5 Octa
Cortex
A15
Cortex
A7

## Slide 9: Agenda
Benchmarks for intra-app diversity
Case study for heterogeneity scenarios

## Slide 10: Intra-App Diversity
Click
Scroll
Type
Read

## Slide 11: User and Processor Activity
Typing
Reading
Scrolling
Launching
Notes: We find that these four types of user actions present distinct computational requirements.
Each graph here represents the instruction per cycle of a user input.
The higher the numbers, the more intensive the computation is.
For example, reading is not computational intensive.
The spikes here are due to background threads of other android tasks.
A mobile benchmark set should include not only the inter-app diversity, but the intra-app diversity as well.

## Slide 12: Benchmarking User Events
Inserting User Inputs
  Use Android Instrumentation to create activities
  Emulate touches, swipes, keyboard events
  Create Android images for gem5 simulation
# Initialize an instrumentation
Instrumentation inst = new Instrumentation();
# Insert a keyboard event
inst.sendKeyDownUpSync(KeyEvent.KEYCODE_A);
Notes: To implement these benchmarks, we create “activities” within Android, loading activity text and pictures locally. We inject touches, swipes, and keyboard events using Android In- strumentation, an API that allows app developers to test their activity windows with emulated user behavior. This method requires access to application source code; our benchmarks are open-sourced.
Other methods use Android MonkeyRunner or write I/O events to the Linux input driver file. However, these methods require a time-stamp for each injected event and precisely specifying the time-stamp to trigger the right event during cycle-accurate, microarchitectural simulation is difficult. Al- ternatively, AutoGUI supports record-replay through VNC and may be useful once it becomes public [33].

## Slide 13: Benchmarks
Interactive
Notes: Sunspider and Linpack are not interactive apps

## Slide 14: Agenda
Benchmarks for intra-app diversity
Case study for heterogeneity scenarios

## Slide 15: Heterogeneity Scenarios
  Processor
    1GHz, 3-issue, 32KB L1, 512KB L2
    Big: out-of-order
    Little: in-order
Shared L1
    Spill state to L1 – 30 cycle transition
L1
registers
registers
Big
Little
Notes: We study three types of interconnections between the big and little cores.
(the other could be power-gated or clock-gated)

## Slide 16: Heterogeneity Scenarios
  Processor
    1GHz, 3-issue, 32KB L1, 512KB L2
    Big: out-of-order
    Little: in-order
Shared L1
    Spill state to L1 – 30 cycle transition
Shared L2
    Flush dirty L1 lines – 500 cycle transition
L1
registers
registers
Big
Little
L1
L2
Notes: We study three types of interconnections between the big and little cores.
(the other could be power-gated or clock-gated)

## Slide 17: Heterogeneity Scenarios
  Processor
    1GHz, 3-issue, 32KB L1, 512KB L2
    Big: out-of-order
    Little: in-order
Shared L1
    Spill state to L1 – 30 cycle transition
Shared L2
    Flush dirty L1 lines – 500 cycle transition
Shared Memory
    Flush dirty L1 / L2 lines – 10K cycle transition
L1
registers
registers
Big
Little
L1
L2
L2
DRAM
Notes: We study three types of interconnections between the big and little cores.
(the other could be power-gated or clock-gated)

## Slide 18: Oracular Transitions
Estimate upper bound on little core utilization
  Obtain big, little performance from oracle.
  Check for profitable transition, given tolerance
* Non-oracular results included in the paper.
Notes: First, the simulation provides the oracle knowledge of the IPC of big and little cores for each interval.
Then, the oracle calculates the transition points such that a transition would not violate the performance penalty.
Then, the oracle applies transition cost to those transition points, and decide whether the resulting IPC will be satisfying. If not, it checks one point after the current point. The process iterates until an ideal transition point is found.

## Slide 19: Little Core Utilization

## Slide 20: Energy Efficiency

## Slide 21: Penalty Tolerance
Tolerance of Performance Penalty (x)
?
Notes: The cross-over point between 30-cy and 500-cy strategies highlights a counter-intuitive observation: sometimes, the 500- cy strategy uses the little core more often.
This is because switching back to the big core is difficult when switching costs are high and performance penalties cannot be tolerated

## Slide 22: Conclusions
Benchmark Design
  Input heterogeneity is critical
  User inputs trigger distinct compute patterns
  Benchmarks should inject diverse inputs
Microarchitectural Design
  User actions shape efficiency gains
  Little cores need performance
  Switching costs are critical for utilization
  https://github.com/schfan/actionbench-

## Slide 23: Evaluating Asymmetric Multiprocessing for Mobile Applications
Songchun Fan, Benjamin Lee
Duke University
Notes: Advisor… computer architecture and resource management
Two projects that I did in the past two years about leveraging heterogeneity for mobile computing

## Slide 24: Q & A
Thank you!

## Slide 25: Backup slides

## Slide 26: Benchmarking Mobile Apps
Current benchmarks neglect user events
BBench
  Automatically loaded webpages for simulators
  A game for testbeds
MobileBench
  Photo viewing, video playback for simulators
Moby
  Email, word processing, maps, social network for simulators

## Slide 27: Core Architectures
Big core = Out-of-Order core
Little core = In-Order core
IPC
Notes: This graph shows that in case of branch mis-predictions, the big core to perform no better than the little core
This is because in out-of-order cores, the cost of branch mis-predictions are higher because the sequence of instructions have been speculated and rescheduled,
And if a miss happens, the big core wastes many cycles to recover from it.
Therefore, if in certain programs these mispredictions happen a lot, a little core is a better choice.

## Slide 28: Core Architectures
Big core = Out-of-Order core
Little core = In-Order core
Big core has higher IPC
Notes: We define an architecture with a big core and a little core.
In reality, they can be a cluster of cores, but for simplicity, in this study we view them as two individual cores of different microarchitectures.
An out of order core contains more components than an in-order core, such as a reorder buffer that can explore the instruction level parallelism,
Therefore it generally has a better performance than an in-order core.
As a cost of those reordering components, it also consumes more power than the in-order core.
Observe the instruction per cycle lines in this graph. The blue line is the IPC of the big core.
It is higher, meaning that in each cycle, a big core can execute more instructions.
However, there are also cases when an in-order core can do same well

## Slide 29: Synchronous Symmetric Multiprocessing
Cores can be at a lower frequency
P=cV2f
http://www.nvidia.com/content/PDF/tegra_white_papers/Benefits-of-Multi-core-CPUs-in-Mobile-Devices_Ver1.2.pdf
NVIDIA Tegra 2, Qualcomm S4 dual,
Samsung Exynos 4, TI OMPA 4...
Notes: In this example, with one core, the single CPU runs at 100% load, requiring 1GHz frequency and 1.1 volt.
With two cores, each core is 50% utilized and requires 550MHz frequency and 0.8volt.
As a result, two cores uses 40% less power than the single core.

## Slide 30: Asynchronous Symmetric Multiprocessing
Cores can be at different frequencies
http://www.brightsideofnews.com/2012/07/25/qualcomm-snapdragon-s4-benchmarking-day/
Qualcomm S800 Series
Notes: Qualcomm took another approach, where cores are connected to different power supplies so that they can run at different frequencies,
Providing more scheduling flexibility and efficiency that the previous approach.
The downside of this approach is the complexity.
Before, all the cores share a single power supply. Now, each core has separate power supply.

## Slide 31: Asymmetric Multiprocessing
Cores can be of different architectures
http://www.brightsideofnews.com/2012/07/25/qualcomm-snapdragon-s4-benchmarking-day/
NVIDIA Tegra 3
Notes: Previous approaches used cores that are same.
Heterogeneous multicores have asymmetric multiprocessing,
Meaning using different microarchitectures,
some cores can be more powerful that other cores.
Nvidia tegra adopts a companion core that is a low power, small core which assists mobile tasks that are lightweight,
While letting the other four big cores to sleep and save power.

## Slide 32: Asymmetric Multiprocessing
Cores can be at different architectures
Samsung Exynos 5 Octa
Notes: Samsung proposed big little architecture. In this design, each processor has two clusters of cores. One cluster of big cores and one cluster of small cores.

## Slide 33: Looking into the future
Lack of proof which architecture is better for mobile CMP
  Does big-little suit mobile apps
  How should it be designed (e.g., interconnections)
Need for realistic benchmarks
Notes: Despite the blooming market and all different solutions of improving energy efficiency,
there is no proof which architecture is most efficient for mobile processors.
Is asymmetric processing, such as big-little, the best approach?
If so, how should it be designed?
In order to quantitatively study mobile processor architectures,
we need realistic applications that represent real user activities.